## Slide 1
IPSec and VPN
Notes: Estimated duration 00:55
Hello Everyone, how are you?
I hope you are doing fine!
Welcome to this new TDP session, I’m glad to see you again.
In this opportunity, I will bring you the VPN basics. I hope that you find it useful.
Before going forward I would like to thank you Daniel, Sabrina and all the TDP team for the excellent work they are doing. I totally recommend you to visit the TDP site and check the previous sessions. They are all very interesting and the knowledge level of the speakers is very high. Definitively the bar is set higher every year and that is thank you to the speakers and your feedback.

## Slide 2
What is a VPN?
Types of VPNs
Commonly used VPNs
IPSec VPNs
Lab
Real scenario troubleshooting
Q&A
Agenda
Notes: Estimated duration 00:55
The agenda for today is the following:
I will start explaining what a VPN is for later tell you what types of VPN are and which are the most commonly used.
After that introduction I will go in deepth into IPSec VPNs.
We will have a strong base of technical theory before moving to the LAB.
Once we finish the LAB ,we will have a troubleshooting space. And finally we will move to the Q&As section.
If you are thinking about having a coffee and grab something to eat, now it is the time

## Slide 3
Agenda
What is a VPN?
Types of VPNs
Commonly used VPNs
IPSec VPNs
Lab
Real scenario troubleshooting
Q&A

## Slide 4: What is a VPN?
Internet
Site A
Site B
Establish a connection between networks over an untrusted network provided via a tunnel
VPN
Notes: Estimated duration 00:40
What is a VPN?
A VPN is a communication path between private sites via an untrusted network
An untrusted network could be Internet, an ISP network, a customer network or an internal network without security.
In a VPN, the original data is encapsulated, encrypted and a new VPN header is added and used for routing
Throughout this session I will use internet for referring to this untrusted network.

## Slide 5
Agenda
What is a VPN?
Types of VPNs
Commonly used VPNs
IPSec VPNs
Lab
Real scenario troubleshooting
Q&A

## Slide 6: Types of VPNs
Site to Site
Remote Access
Notes: Estimated duration 00:10
There are 2 types of VPNs. Site to site VPNs and Remote Access VPNs

## Slide 7: Types of VPNs
Site to Site
Remote Access
Internet
Site A
Site B
Data A-B
Data A-B
Data A-B
Data A-B
Data A-B
Data A-B
Notes: Estimated duration 01:15
As the name states, Site to site VPN connects two sites.
The VPN tunnel can be up permanently or can be generated on demand when traffic needs to flow to the remote site.
In the picture you can see the original data from network A network B in site B in black.
The original data is encapsulated and encrypted on the VPN gateway with a new VPN Header. That VPN header is the green one in the picture and you can see that the original data is inside that new packet as payload data.
This new VPN IP header has the VPN peers as source/destination IP addresses, not the originalIPs (Green packet in the drawing). That header is used to transport the information over the untrusted network until It reaches the remote VPN peer.
The remote VPN peer decapsulates and decripts the packet and forwards the original data to the destination.

## Slide 8: Types of VPNs
Internet
Site to Site
Remote Access
Site A
User 1
User 2
User n
Notes: Estimated duration 00:45
Remote Access VPN is used for provide access for remote users or systems to sites/systems. This scenario is similar to old remote dial-up scenarios.
Users can be mobile users, desktop users, servers, etc
This scenario it is most commonly used for mobile users.
The user has a VPN client application installed on its PC and it is used to connect to the Main site for access to resources.
The traffic towards the main site is encrypted in the same way as site to site VPN
This is how we connect to AT&T network from our PC when doing home work.

## Slide 9
Agenda
What is a VPN?
Types of VPNs
Commonly used VPNs
IPSec VPNs
Lab
Real scenario troubleshooting
Q&A

## Slide 10: Commonly used VPNs
L2 VPNs
    L2TP
    MPLS VPN. VPLS
L3 VPNs
      IPSec
      MPLS VPN. Routed
      GRE
L5/L6 VPNs
    SSL-TLS
Notes: Estimated duration 01:00
There are a lot of VPN types used in the real life. The difference between them is how they encapulate and/or encrypt data and what kind of data can they manage, but the main operation idea is the same for all of them, provide a connection over untrusted networks.
Here I mention some of the most commonly used VPNs. I will not get through in detail on each of them but I just mention them to give you an idea about on which layer they operate.
L2 VPNs
    L2TP
    MPLS VPN. VPLS
L3 VPNs
  IPSec
  MPLS VPN. Routed
  GRE
L5/L6 VPNs
    SSL-TLS

## Slide 11
Agenda
What is a VPN?
Types of VPNs
Commonly used VPNs
IPSec VPNs
Lab
Real scenario troubleshooting
Q&A
Notes: Well, fasten your seat belts and take a deep breath because we will start with IP Sec.
Estimated duration 00:55
Estimated duration 00:40
Estimated duration 00:55
Estimated duration 00:40
Estimated duration 00:10
Estimated duration 01:15
Estimated duration 00:45
Estimated duration 01:00
Estimated total time so far: 7 minutes

## Slide 12: IPSec VPN
IP Security.
RFC: A lot!. Starts at 2401
Works at IP Layer (L3)
Supports ONLY unicast traffic
2 modes
    Tunnel mode
    Transport mode
2 protocols
    ESP. Encapsulation Security Payload
    AH. Authentication Header
2 Phases
    Phase 1: Establishes a secure connection channel for Phase 2
    Phase 2: Establishes a secure connection channel for IPSec
Notes: Estimated duration 02:45
IP Security (IPSec) is a protocol for providing IP data security and integrity services for IPv4 and IPv6
It is defined on RFC 2401 but as it uses many protocols for VPN establishment. There are a lot of more RFCs for those.
(like 2402, 2406, 2408, and so on)
Works at IP layer
Supports only unicast traffic. Because these services are provided at the IP layer, they can be used by any higher layer protocol, e.g., TCP, UDP, ICMP, BGP, etc.
It supports 2 modes of operation: tunnel mode and transport mode
Tunnel mode:
  It protects the entire IP packet. Is most commonly used between gateways, or at an end-station to a gateway, the gateway acting as a proxy for the hosts behind it.
In transport mode it provides protection primarily for upper layer protocols.
When transport mode is used, IPSec encrypts only the IP payload, not the entire IP packet. Is used between end-stations or between an end-station and a gateway, if the gateway is being treated as a host.
IPSec uses two protocols to provide traffic security
  Encapsulation Security Payload – ESP.
  Authentication Header- AH.
  ESP
  ESP encapsulates the entire IP packet and adds a new VPN IP header. It is defined in RFC 2406
  IP Protocol number 50
  Provides
    Data confidentiality
    Data integrity
    Data origin authentication
    Anti-replay services
  Can be used in tunnel and transport mode
  AH
  AH encapsulates the payload of the IP packet and adds a new VPN IP header but uses the original IP header for routing. defined in RFC 2402
  Protocol number 51
  Provides
    Data integrity
    Data origin authentication
    Anti-replay services
  Can be used in tunnel and transport mode
Establishing an IPSec session it is 2 phase process:
    Phase 1: Establishes a secure connection channel for Phase 2 negotiations
    Phase 2: Establishes a secure connection channel for IPSec secure communication

## Slide 13: IPSec VPN: Benefits
Anti Replay
Confidentiality
Integrity
Authentication
Notes: Estimated duration 01:15
A VPN is secure because private data is encapsulated, encrypted and sent to the remote peer for decryption/de capsulation.
We will later see what encapsulation and encryption is.
There are four major concerns when sending private data over a public medium that IPSec addresses.
One is Anti-replay It Ensures the uniqueness of each IP packet. Anti-replay is also called replay prevention. Anti-replay ensures that data captured by an attacker cannot be reused or replayed to establish a session or gain information illegally.
Confidentiality
Keep data secure and hidden (using Encryption). Ensures that data is only disclosed to intended recipients.
Integrity
Ensure data hasn’t been changed. Protects data from unauthorized modification in transit, ensuring that the data received is exactly the same as the data sent.
Authentication
Verifies if did the traffic really come from the advertised source?
Verifies that a message could only have been sent from a computer that has knowledge of the authentication key
---------------------------------------------------------------------------------------------------------------------
The set of security services offered includes access control, connectionless integrity, data origin authentication, protection against replays (a form of partial sequence integrity), confidentiality (encryption), and limited traffic flow confidentiality.

## Slide 14: IPSec encapsulation
ESP. Tunnel mode
ESP. Transport mode
AH. Tunnel mode
AH. Transport mode
Notes: Estimated duration 01:45
In this diagram you can see how the IP packet is modified on each IPSec mode usage.
AH in transport mode only adds a new authentication header after the IP header.
In tunnel mode, AH signs the entire IP packet.
-----But not all the IP header fields. There are some fields that need to change like TTL and ToS.
Both AH modes are most used for integrity checks to verify that the IP packet was not modified.
ESP in transport mode only encapsulates the IP payload in an ESP header/trailer
ESP in tunnel mode encapsulates and encrypts the IP payload and also Signs the entire ESP header plus the IP payload
Encapsulation is the process of taking a data and add it into a new format data format
Lets take the example of ESP protocol mode. ESP takes the original IP payload and adds it into a new ESP header and trailer. The IP addresses of the original IP header (who are the ones who belong to the end hosts) are now on the ESP header. The IP header IP addresses are new IP addresses of the VPN peers.
When a devices receives the entire IP packet, it processes first at IP layer, removes the IP header and then process the ESP header for later examine the original IP payload.

## Slide 15: IPSec VPN: Phase 1
Builds on ISAKMP and OAKLEY protocols
Internet Key Exchange (IKE) protocol
Protocol UDP, port 500
2 Modes:
    Main
    Aggressive
Parameters
    Encryption
    Integrity
    Diffie-Hellman group
    Timeout
    Authentication
Notes: Estimated duration 05:00
As I told you before, for establishing an IPSec VPN tunnel we need to configure 2 phases.
Phase 1: Establishes a secure connection channel for Phase 2 negotiations
Phase 1 builds on ISAKMP and OAKLEY protocols
(ISAKMP) The Internet Security Association and Key Management Protocol defines the procedures and packet formats to establish, negotiate, modify and delete Security Associations (SA)
This is needed because in a VPN there is a lot of background work related to key generation and management that it is complex to configure if you want to do it manually.
ISAKMP formats provide a consistent framework for transferring key and authentication data which is independent of the key generation technique, encryption algorithm and authentication mechanism.
ISAKMP cleanly separate the details of security association management (and key management) from the details of key exchange.
There may be many different key exchange protocols, each with different security properties. However, a common framework is required for agreeing to the format of SA attributes, and for negotiating, modifying, and deleting SAs. ISAKMP serves as this common framework.
A Security Association (SA) is a relationship between two or more entities that describes how the entities will utilize security services to communicate securely
A security association (SA) is a set of policy and key(s) used to protect information. The ISAKMP SA is the shared policy and key(s) used by the negotiating peers in this protocol to protect their communication
Phase 1 uses Internet Key Exchange (IKE) protocol to negotiate, and provide authenticated keying material for, security associations in a protected manner. IKE uses udp protocol 500
Phase 1 is where the two ISAKMP peers establish a secure, authenticated channel with which to communicate. This is called the ISAKMP Security Association (SA)
Establishes Security Associations for Phase 2 negotiated services
The ISAKMP SA is bi-directional. That is, once established, either party may initiate Phase 2 negotiations
Main mode: in main mode the initiator and the requester exchanges 6 messages before having a established SA
Aggressive mode: : in Aggressive mode the initiator and the requester exchanges 3 messages before having a established SA
Main mode is more secure than aggressive mode
Main mode – used when both tunnel peers have static IP addresses configured
Aggressive mode – used when one tunnel peer has a dynamically-assigned IP address
To sum up, Phase 1 is IKE where you start things out...
You will configure the encryption algorithm, the integrity hash, the diffie-hellkman group, the timeout and the authentication mode.
We will see all those parameters options later.
You can define many Phase 1 policies in the sender and all will be sent to the receiver, but it will only choose one.
-------------------------------------------------------------------------------------------------------------------------------------------
Adicional para mi
--------------------------------------------------------------------------------------------------------------------------
Negotiates proposals containing encryption and authentication algorithms
Creates Encryption and Authentication Keys automatically which provides ability to be re-keyed frequently
Provides gateway identity function
After the basic set of security attributes has been agreed upon, initial identity authenticated, and required keys generated, the established SA can be used for subsequent communications by the entity that invoked ISAKMP.
Key Establishment (Key Generation / Key Transport): The two common methods of using public key cryptography for key establishment are key transport and key generation
An example of key transport is the use of the RSA algorithm to encrypt a randomly generated session key (for encrypting subsequent communications) with the recipient's public key. The encrypted random key is then sent to the recipient, who decrypts it using his private key
The Diffie-Hellman (D-H) algorithm illustrates key generation using public key cryptography. The D-H algorithm is begun by two users exchanging public information. Each user then mathematically combines the other's public information along with their own secret information to compute a shared secret value. This secret value can be used as a session key or as a key encryption key for encrypting a randomly generated session key. This method generates a session key based on public and secret information held by both users. The benefit of the D-H algorithm is that the key used for encrypting messages is based on information held by both users and the independence of keys from one key exchange to another provides perfect forward secrecy.

## Slide 16: IPSec VPN: Phase 2
IPSec Parameters
    Protocol: ESP or AH
    Encryption: Transform set
    Integrity: Transform set
    Proxy: interesting traffic
    Lifetime: SA regeneration time
    Peer: endpoint
    Optional: Perfect Forward Secrecy (PFS)
Notes: Estimated duration 02:00
Phase 2 is where Security Associations are negotiated on behalf of upper services .
Phase 2 is IPSec where you get into what specifics you set up in your policies to have your keys set. This is the traffic keys themselves. And the traffic is getting encrypted here. IPSec SA is present if everything goes well.
Security Associations are negotiated using a Phase 1 secure channel
  Phase 2 is called Quick Mode
  Phase 2 uses ESP or AH protocols to protect traffic.
Phase2 SA are unidirectional, therefore 2 SAs needs to be established. One for outgoing traffic and one for incoming traffic.
To establish a Phase 2 you need to define
the encryption algorithm
The integrity hash
The Proxy: interesting traffic for encryption identified using an ACL
SA lifetime
Remote peer ID
And optionally PFS, perfect forward secrecy. PFS is Diffie-Hellman applied on Phase 2 for key generation.
The Diffie-Hellman (D-H) algorithm illustrates key generation using public key cryptography. The D-H algorithm is begun by two users exchanging public information. Each user then mathematically combines the other's public information along with their own secret information to compute a shared secret value. This secret value can be used as a session key or as a key encryption key for encrypting a randomly generated session key.
---------------------------------------------------------------------------------------------------------------------------------------------------------
Protection suite of priority 1
encryption algorithm: Three key triple DES
hash algorithm: Secure Hash Standard
authentication method: Pre-Shared Key
Diffie-Hellman group: #1 (768 bit)
lifetime: 86400 seconds, no volume limit
Default protection suite
encryption algorithm: DES - Data Encryption Standard (56 bit keys).
hash algorithm: Secure Hash Standard
authentication method: Rivest-Shamir-Adleman Signature
Diffie-Hellman group: #1 (768 bit)
lifetime: 86400 seconds, no volume limit

## Slide 17: IPSec VPN: concepts
Encryption
Integrity
Keys
Notes: Estimated duration 07:00
+
Estimated duration 02:45
Estimated duration 01:15
Estimated duration 01:45
Estimated duration 05:00
Estimated duration 02:00
Total estimated time 20:00

## Slide 18: Encryption Process
Encryption Algorithm
Data: www.att.com
Data: das$s.1O9&f
Encryption key
Encryption key
Notes: Estimated duration 01:00
Encryption is the process of encoding messages or information in such a way that only authorized parties can read it.
The original data is encrypted using an encryption algorithm and a key. The receiver can only read the data if it has the key to decrypt it.
This way, if the data is captured it can only be read if you have the encryption key.
Using a long complex key is recommended in conjunction with a strong encryption algorithm.
Some common encryption algorithms are:
DES
3DES
AES 128, 256
RSA
As you can see in the presentation, after applying the encryption algorithm, the data is changed and there is no way that you can know that the encrypted data with www.att.com

## Slide 19: Hash Process. (HMAC)
If the hash values match, the data is good
5
2
3
4
1
If the hash values match, the data is good
Data
HASH
Data
Sender
Receiver
HASH
Data
HASH
HASH
HASH
Data
Hash Algorithm
Hash Algorithm
Notes: Estimated duration 02:00
Hash message authentication codes (HMAC) sign packets to verify that the information received is exactly the same as the information sent. This is called integrity. HMACs provide integrity through a keyed hash, the result of a mathematical calculation on a message using a hash function combined with a shared, secret key. (a hash function is an algorithm)
The sender takes the data and applies the hash algorithm. The result Hash is appended to the data and then the entire information is sent to the receiver.
The receiver receives the data + hash and separates them. Then it takes the separated data and applies the hash algorithm. As a result, it will have a HASH value for the same data. Finally it compares both Hashes, the one generated by itself and the one received from the sender. If they are equal, then the data was not modified.
Examples
  MD5, SHA
    MD5 provides 128 bit output
    SHA provides 160 bit output
For integrity, you can choose between two hash functions when setting policy:
MD5 Message Digest 5 (MD5) is based on RFC 1321. MD5 completes four passes over the data blocks, using a different numeric constant for each word in the message on each pass. The number of 32-bit constants used during the MD5 computation ultimately produces a 128-bit hash that is used for the integrity check.
SHA1 Secure Hash Algorithm 1 (SHA1) was developed by the National Institute of Standards and Technology as described in Federal Information Processing Standard (FIPS) PUB 180-1. The SHA process is closely modeled after MD5. The SHA1 computation results in a 160-bit hash that is used for the integrity check. Because longer hash lengths provide greater security, SHA is stronger than MD5

## Slide 20: Symmetric key encryption
Symmetric keys are faster and used for bulk data encryption
Typical key size vary from 40bits to 2048 bits
Examples: DES, 3DES, AES
1
2
3
Sender
Receiver
+
+
Original data
Encrypted data
Encrypted data
Original data
Notes: Estimated duration 01:00
You can use pre shared keys for the encryption process. Pre shared means that the parties agree on a shared, secret key that is used for encryption /decryption of data.
A pre shared key is a symmetric key
IPSec can use pre shared keys for authentication of the peers.

## Slide 21: Public key encryption
Public and Private key scheme
Slow when used for data encryption
Examples: RSA, DH
Pub
Priv
1
+
2
+
4
Pub
Pub
Sender
Receiver
Original data
Original data
Encrypted data
Encrypted data
3
Notes: Estimated duration 02:00
Public-key cryptography, also known as asymmetric cryptography, is a class of cryptographic algorithms which requires two separate keys, one of which is secret (or private) and one of which is public. Although different, the two parts of this key pair are mathematically linked.
The receiver generates 2 keys, one private and one public. The traffic encrypted using the public key can only be decrypted with the private key and vice versa.
The receiver sends its public key to the sender. The sender will use that public key to encrypt traffic. The receiver will decrypt that traffic using its private key.
Asymmetric (public) key: certificates
Ipsec VPN uses Asymetric key
Provides data confidentiality
Data is encrypted and decrypted by using keys
  Symmetric (secret) key
  Asymmetric (public) key
Symmetric (secret) key: pre shared keys

## Slide 22
Agenda
What is a VPN?
Types of VPNs
Commonly used VPNs
IPSec VPNs
Lab
Real scenario troubleshooting
Q&A

## Slide 23: LAB
Internet
Site B
192.168.1.0/24
Site to site IPSec VPN
Pre shared key authentication
Site A
10.10.1.0/24
1.1.1.2
2.2.2.2
2.2.2.1
1.1.1.1
Notes: In this lab we will establish a VPN tunnel between 2 private networks over a public network.
On the left side we have Site A with private network 10.10.1.0/24. The VPN gateway is a Cisco ASA FW and it is connected to internet.
On the right side we have site B with private network 192.168.1.0/24. The VPN gateway is a Cisco 7600 router.
Internet is simulated with a WAN router that connects 2 public networks.

## Slide 24
LAB config: Cisco ASA v8.4
!
!PHASE 1
!
tunnel-group 2.2.2.2 type ipsec-l2l
tunnel-group 2.2.2.2 ipsec-attributes
pre-shared-key 1234567890
!
crypto ikev1 policy 10
authentication pre-share
encryption aes
hash md5
group 2
lifetime 86400
crypto ikev1 enable outside
!
!PHASE 2
!
access-list cptomap_vpn_siteb extended permit ip 10.10.1.0 255.255.255.0 192.168.1.0 255.255.255.0
!
crypto ipsec security-association lifetime seconds 28800
crypto ipsec security-association lifetime kilobytes 4608000
crypto ipsec ikev1 transform-set ESP-3DES-MD5 esp-3des esp-md5-hmac
!
crypto map cptomap_outside 10 match address cptomap_vpn_siteb
crypto map cptomap_outside 10 set peer 2.2.2.2
crypto map cptomap_outside 10 set transform-set ESP-3DES-MD5
!
crypto map cptomap_outside interface outside
!

## Slide 25
LAB config: Cisco IOS v15.1
!
!PHASE 1
!
crypto isakmp policy 10
encryption aes 128
hash md5
group 2
authentication pre-share
lifetime 86400
!
crypto isakmp key 1234567890 address 1.1.1.2
!
!
!PHASE 2
!
ip access-list extended cptomap_vpn_sitea
permit ip 192.168.1.0 0.0.0.255 10.10.1.0 0.0.0.255
!
crypto ipsec transform-set ESP-3DES-MD5 esp-3des esp-md5-hmac
mode tunnel
!
crypto map cptomap_outside local-address fastethernet 0/0
crypto map cptomap_outside 10 ipsec-isakmp
match address cptomap_vpn_sitea
set peer 1.1.1.2
set transform-set ESP-3DES-MD5
!
interface fastethernet 0/0
crypto map cptomap_outside
!

## Slide 26
LAB config: Verification commands
!
! PHASE 1
!
Show crypto ikev1 sa
Show crypto ikev1 sa detail
!
!PHASE 2
!
Show crypto ipsec sa
Show crypto ipsec sa detail
Show crypto condition peer x.x.x.x
Show crypto session (IOS)
!

## Slide 27
Agenda
What is a VPN?
Types of VPNs
Commonly used VPNs
IPSec VPNs
Lab
Real scenario troubleshooting
Q&A

## Slide 28: Troubleshooting
Check Pre shared key
Check ACLs
Check Phase 1 parameters
Check Phase 2 parameters
Check routes to remote network
Verify that ISAKMP-IKE/crypto map is enabled on interfaces
Verify that ISAKMP and ESP traffic is allowed
Debug
Check internal port openings
Check NAT translations
Don’t assume, CHECK. Check the config, and RE CHECK the config again! Be prepared for guiding the other end through the verification/debug process
Notes: MM_ACTIVE
QM_IDLE
debug
IKE_DECODE SENDING
IKE_DECODE RECEIVED
MM_WAIT_MSG2, MM_WAIT_MSG4, MM_WAIT_MSG6

## Slide 29
Q&A

## Slide 30
Thank You!